## Slide 1: Class Diagram, Flowchart, and Documentation
Started on 15 April 2025

## Slide 2: Credentials
For EMQX, InfluxDB, Grafana web interface:
  username: root
  password: root1234
EMQX Broker – [IP address]:1883
EMQX Broker dashboard - [IP address]:18083
InfluxDB dashboard - [IP address]:8086
Grafana dashboard - [IP address]:3000

## Slide 3: Class Diagram (Simple)
flow_monitor
gps_config
deviceId
session
system_state
slot7_state
time
IoT Box

## Slide 4: Class Diagram
For MQTT messages sent by Smart Box, fan and flow monitor variables were formatted for InfluxDB compatibility. See [Example MQTT Messages] slides for the original variables. See flatten_dict() for formatting method.
Currently, the API misspells the bold variables as cpuUsaged, memUsaged, storageUsaged, and humitidy respectively. Pending fix.

## Slide 5: Connection Handshake
Example connect
{
"type": "connect",
"version": 1,
"session": "125b162f-9c01-4a4b-8000-0ec3256ff69d",
"deviceId": "smartBox_0c7124300bc7fb4e1ceb4acdb7162d74",
"time": 1746494252,
"data": {
"securityMode": [
"none",
"static",
"ecdh"
]
}
}
Example connect_reply
{
"type": "connect_reply",
"version": 1,
"session": "125b162f-9c01-4a4b-8000-0ec3256ff69d",
"deviceId": "smartBox_0c7124300bc7fb4e1ceb4acdb7162d74",
"time": 1746494252,
"response": {
"code": 0,
"message": "success"
},
"data": {
"security": "none"
}
}

## Slide 6: Slot7_state
Command
{
“type": "command",
"version": 1,
"session": [session],
"deviceId": [deviceId],
"time": [time],
"data": {
"service": "slot7",
"method": "state",
"parms": {}
}
}
Example command_reply
{
"type": "command_reply",
"version": 1,
"session": "8ae05cc8-dee3-45c9-a72d-4a82bef84765",
"deviceId": "smartBox_56b6440c6e7421e397737893aeb2a36f",
"time": 1744777012,
"response": {
"code": 0,
"message": {
"spdAlert": false,
"spdSurge": 0,
"ardState": true,
"ardAlert": false,
"ardVoltage": 242,
"ardCurrent": 160,
"autoLight": false,
"doorState": true,
"lightState": true,
"heaterState": false,
"waterAlert": false,
"fan": [
{
"id": 1,
"fanSpeed": 30,
"fanAlert": false,
"fanState": false
}
]
}
}
}

## Slide 7: Flow_monitor
Command
{
“type": "command",
"version": 1,
"session": [session],
"deviceId": [deviceId],
"time": [time],
"data": {
"service": "switch.port",
"method": "statistics",
"parms": {
}
}
Example command_reply
{
"type": "command_reply",
"version": 1,
"session": "ec21db29-1e96-4ef7-ac7c-b59c75830cb5",
"deviceId": "smartBox_dcbbfa35c8e5fcd179f84118a2d00254",
"time": 1744777012,
"response": [
{
"id": 1,
"name": "port1",
"rxByte": "363829",
"txByte": "563446",
"rxPacket": 1222,
"txPacket": 1523,
"rxError": 0,
"txError": 0
},
{
"id": 2,
"name": "port2",
"rxByte": "6603229",
"txByte": "22849802",
"rxPacket": 48755,
"txPacket": 36213,
"rxError": 0,
"txError": 0
},
{
"id": 3,
"name": "port3",
"rxByte": "0",
"txByte": "0",
"rxPacket": 0,
"txPacket": 0,
"rxError": 0,
"txError": 0
},
{
"id": 4,
"name": "port4",
"rxByte": "0",
"txByte": "0",
"rxPacket": 0,
"txPacket": 0,
"rxError": 0,
"txError": 0
},
{
"id": 5,
"name": "port5",
"rxByte": "0",
"txByte": "0",
"rxPacket": 0,
"txPacket": 0,
"rxError": 0,
"txError": 0
},
{
"id": 6,
"name": "port6",
"rxByte": "0",
"txByte": "0",
"rxPacket": 0,
"txPacket": 0,
"rxError": 0,
"txError": 0
},
{
"id": 7,
"name": "port7",
"rxByte": "0",
"txByte": "0",
"rxPacket": 0,
"txPacket": 0,
"rxError": 0,
"txError": 0
},
{
"id": 8,
"name": "port8",
"rxByte": "0",
"txByte": "0",
"rxPacket": 0,
"txPacket": 0,
"rxError": 0,
"txError": 0
},
{
"id": 9,
"name": "port9",
"rxByte": "0",
"txByte": "0",
"rxPacket": 0,
"txPacket": 0,
"rxError": 0,
"txError": 0
},
{
"id": 10,
"name": "port10",
"rxByte": "0",
"txByte": "0",
"rxPacket": 0,
"txPacket": 0,
"rxError": 0,
"txError": 0
}
]
}

## Slide 8: System_state
Command
{
“type": "command",
"version": 1,
"session": [session],
"deviceId": [deviceId],
"time": [time],
"data": {
"service": "system",
"method": "state",
"parms": {}
}
}
Example command_reply
{
"type": "command_reply",
"version": 1,
"session": "ec21db29-1e96-4ef7-ac7c-b59c75830cb5",
"deviceId": "smartBox_dcbbfa35c8e5fcd179f84118a2d00254",
"time": 1744777012,
"response": {
"code": 0,
"message": {
"dateTime": 1744805812,
"runTime": 7925,
"cpuUsaged": 9797,
"memTotalSize": 246452,
"memFreeSize": 173616,
"memUsaged": 2955,
"storageTotalSize": 1997240,
"storageFreeSize": 1990896,
"storageUsaged": 31,
"temperature": 29,
"humitidy": 51,
"poeRealPower": 0
}
}
}

## Slide 9: Gps_config
Command
{
“type": "command",
"version": 1,
"session": [session],
"deviceId": [deviceId],
"time": [time],
"data": {
"service": "netdmate",
"method": "mobile.gpsGet",
"parms": {"name": "lte1"}
}
}
Example command_reply
{
"type": "command_reply",
"version": 1,
"session": "ec21db29-1e96-4ef7-ac7c-b59c75830cb5",
"deviceId": "smartBox_dcbbfa35c8e5fcd179f84118a2d00254",
"time": 1744777012,
"response": {
"latitude": 1.4531,
"latitude_h": "N",
"longitude": 103.792291,
"longitude_h": "E",
"altitude": 62.6,
"altitude_u": "M"
}
}

## Slide 10: Start up NMS 2.0
Open Docker Desktop (Docker engine must be running)
Open Terminal on Docker Desktop or cmd
cd to nms2 folder directory
Enter “docker compose up -d --build”
Open Grafana in web browser using [IP address]:3000 (any device connected to NMS 2.0 computer via TCP can open Grafana page)
See 1 Demo Video (Startup)

## Slide 11: NMS 2.0 Diagnostics
  Docker Desktop for container/service status
  Terminal or cmd > Enter “docker attach python_app” to view Python app.py terminal output containing logs
  Ensure Smart Boxes have NMS 2.0 computer’s IP address set as an MqttBroker address
  See 2 Demo Video (Diagnostics) and 2.5 Demo Video (Smart Box)

## Slide 12: Navigate NMS 2.0
  Filter devices using deviceId dropdown list
  Navigate different dashboards using Navigate to Page button
  See 3 Demo Video (Navigation)

## Slide 13: Shutdown NMS 2.0
Depending on use case, use one of the following:
Stop only python_app by selecting python terminal, then enter Ctrl+C (KeyboardInterrupt is coded to stop threads safely).
Stop NMS 2.0 by entering “docker compose stop” in regular terminal/cmd, then “docker compose start” to restart.
Delete NMS 2.0 container (not local files) by entering “docker compose down” in regular terminal/cmd.
You can now make changes to nms2 files, then “docker compose up” to rebuild the updated app and see the changes.
See 4 Demo Video (Shutdown)

## Slide 14: Connection Handshake Flowchart
See Slide 10